## Slide 1
Hybrid Prognostic Approach for Micro-Electro-Mechanical Systems
Haithem Skima, Kamal Medjaher, Christophe Varnier, Eugen Dedu and Julien Bourgeois
haithem.skima@femto-st.fr
FEMTO-ST Institute, Besançon – France

## Slide 2
Outline
Introduction
State of the art
PHM of MEMS
Simulation results
Conclusion and perspectives
H. Skima, K. Medjaher, C. Varnier, E. Dedu, J. Bourgeois, IEEE Aerospace Conference, March 7-14, 2015

## Slide 3
Health Indicator
Time (t)
tc
Failure threshold
tf
RUL
Introduction
Introduction State of the art PHM of MEMS Simulation results Conclusion
Prognostics & Health Management (PHM)
Process that monitors systems, assesses their health state, detects and diagnoses their faults, anticipates the time to failures by calculating the remaining useful life (RUL) and takes appropriate decisions accordingly.
Micro-Electro-Mechanical Systems (MEMS)
A MEMS is a micro-system that integrates mechanical components using electricity as source of energy in order to perform measurement functions and / or operating in structure having micrometric dimensions.
Examples of application

## Slide 4
Introduction
Applications: Automotive, aerospace, biomedical, optical, fluidic, communication technologies…
Introduction State of the art PHM of MEMS Simulation results Conclusion
Categories of MEMS
Bio MEMS
Micro sensors
Micro actuators
RF MEMS
MOEMS
Others
Categories of MEMS

## Slide 5
Introduction
Introduction State of the art PHM of MEMS Simulation results Conclusion
Reliability issues
Degradations: loss of performances
Faults: non delivered services / non achieved functions
 risk of accidents
PHM of MEMS
Motivation
Improve the reliability and availability of systems containing MEMS
Avoid failures
Reduce maintenance costs

## Slide 6
[H. R. Shea, M. McMahon et al., J. Ruan et al., R. Mûller-Fiedler et al.]
Introduction State of the art PHM of MEMS Simulation results Conclusion
State of the art
Failure mechanisms
Mechanical | Electrical | Material
Delamination, Fracture, Fatigue, Creep, Stiction, Plastic-deformation, Adhesion | Degradation of dielectrics, Electrostatic discharge ESD Electro-migration, Electrical short Circuit, Electrical stiction | Stiction, Contamination
Related to utilization | Related to manufacturing
Stiction, Delamination, Fatigue, Creep, Fracture, Adhesion, ESD, Electro-migration, Electrical short circuit | Stiction, Contamination, Fracture, Electrical short circuit
[M. MATMAT 2010]
Mechanical, electrical and material based failure mechanisms
Failure mechanisms related to manufacturing or to utilization
Influence factors: temperature, humidity, vibration, noise, dust, shocks, overcharges …

## Slide 7
Stiction of the finger on the substrate [Tanner et al.]
Stiction in electro-thermal actuator
[M. Dardalhon]
Micro-actuator finger fracture
[ B. Charlot]
Contamination in a comb-drive [Tanner et al.]
Introduction State of the art PHM of MEMS Simulation results Conclusion
Failure mechanisms
State of the art

## Slide 8
Design and fabrication of MEMS
Testability and characterization of MEMS
Identification and understanding of failure mechanisms
Design, fabrication and packaging optimization
Accelerated life tests to develop reliability models
Statistical studies of failures on a significant number
of samples
Introduction State of the art PHM of MEMS Simulation results Conclusion
State of the art
Reliability of MEMS

## Slide 9
State of the art
Given conditions and period of time
The predictive reliability models are obtained from statistical data
      Significant number of samples
      Reliability models are not personalized for each MEMS and therefore there is no update of the model parameters during their utilization
Introduction State of the art PHM of MEMS Simulation results Conclusion
Assess the health state of the MEMS at any time (Health assessment)
Predict the Remaining Useful Life (RUL) by taking into account the current and the future conditions
Update the degradation models parameters based on monitoring data
    Anticipate failures in a system based on MEMS and optimize decision making
Reliability limitations
PHM

## Slide 10
PHM of MEMS
Construction of the nominal behavior model
Generation of the degradation model
Health assessment and prediction
Definition of the failure thresholds
&
RUL estimation
&
Decision making
Operating conditions
Synoptic of the proposed approach
Introduction State of the art PHM of MEMS Simulation results Conclusion

## Slide 11
Voltage supplier
Computer
Light source
Arduino
NI card
Resistors
Camera
MEMS
Anti-vibration table
Experimental platform
PHM of MEMS
Introduction State of the art PHM of MEMS Simulation results Conclusion

## Slide 12
Designed to control flow rates or pressure with high precision and with fast response time
Electrical connections
Movable membrane
Fluid connection ports
MEMS valve
PHM of MEMS
Introduction State of the art PHM of MEMS Simulation results Conclusion
Normally open
Common port
Normally closed
Normally open
Common port
Normally closed
Scanning Electron Microscope (SEM) pictures (FEMTO-ST)

## Slide 13
Introduction State of the art PHM of MEMS Simulation results Conclusion
PHM of MEMS
Time response of the MEMS
Support used to fix the MEMS

## Slide 14
Deflection
Anchorage
Anchorage
ᶿ
PHM of MEMS
Nominal behavior model
Introduction State of the art PHM of MEMS Simulation results Conclusion
↔
State representation:
Canonical transfer function:

## Slide 15
PHM of MEMS
Introduction State of the art PHM of MEMS Simulation results Conclusion
Why ?
  Manufacturer guarantees 10 million cycles without significant performance loss
  With a square wave (frequency= 1 Hz), the MEMS performs 86200 cycles per day
   Approximately 3 months to observe significant drift of the performance
  To show the effectiveness of the proposed method
  Simulated degradation models
  The variation of the parameters depend on the variation of the stiffness k
  Degradation models of the MEMS valve represented by the variation of the stiffness k
Exponential degradation:
Polynomial degradation:
Simulation of degradation
  Simulations are performed on Matlab

## Slide 16
Introduction State of the art PHM of MEMS Simulation results Conclusion
Simulation results
Polynomial degradation
Notes: - The injection of these degradation models in the nominal behavior model leads to a global model. By analyzing the response time given by this model, the parameters of the system can be estimated at each time and then the health state can be obtained
We see here the impact of the degradation model on the response time. I have plotted three responses time for 3 different values of stiffness K

## Slide 17
Introduction State of the art PHM of MEMS Simulation results Conclusion
Simulation results
Exponential degradation
Notes: The same thing for the exponential degradation model, we see the impact on the response time of the system

## Slide 18
Introduction State of the art PHM of MEMS Simulation results Conclusion
Simulation results
RUL estimation
Definition of the failure thresholds:
: time that corresponds to the limit stiffness value beyond which the MEMS can be considered as out of service

## Slide 19
Conclusion
Introduction State of the art PHM of MEMS Simulation results Conclusion
Implement PHM on MEMS
Hybrid Prognostic approach proposed
Experimental measurements performed
Nominal behavior of the MEMS valve derived
Simulation results showed the effectiveness of the proposed method
Experiments are still ongoing to derive the degradation models which will allow to estimate the health state of the MEMS and predict their RUL
Optimize the performance and the availability of a distributed system containing numerous MEMS
Ongoing and future works

## Slide 20
Thank you for your attention
H. Skima, K. Medjaher, C. Varnier, E. Dedu, J. Bourgeois, IEEE Aerospace Conference, March 7-14, 2015