## Slide 1: Network Parameter Influence on Communications in Dense Wireless Nanonetworks
Carole Al Mawla
Eugen Dedu
Université de Franche-Comté, CNRS, institut FEMTO-ST, France
ACM NanoCom 2024
Milan, Italy, October 28–30, 2024
Lebanese University
Faculty of science

## Slide 2: Plan
Wireless nanonetwork
Routing protocol
Network parameters influence
Conclusion & Future work
01
02
03
05
1 / 16

## Slide 3
Wireless nanonetwork
01
Carole Al Mawla
2 / 16

## Slide 4: Wireless nanonetwork
Hundreds or thousands of tiny nodes called nanonodes
Nanonode size is less than 1 micrometer (1 to 1000 nanometers)
Nanonode limitations:
  Simple computing, sensing, and actuation
  Low resources (CPU, memory, battery) due to fabrication constraints
  Low network lifetime because of energy/battery limitation
Carole Al Mawla
01
3 / 16
Routing protocol
Notes: A wireless nanonetwork is composed of hundreds or thousands of tiny nodes called nanonode
These nanonodes are of size less than 1 micrometer and has lots of limitations like ….
Note that a good wireless nanonetwork is reflect by its routing protocol

## Slide 5
Routing protocol
02
Carole Al Mawla
4 / 16

## Slide 6: Routing protocol
A good routing protocol in a multi-hop network:
    Selects the best path through the network from the source to the destination
This is not enough
Good protocol also needs optimal network parameters
S
D
02
5 / 16
Notes: The well knowing concept of a good routing protocol is influenced by how the protocol select the most optimal path through the network from the source to the destination
Here we are showing that not a good routing protocol might give different consequences on network if the parameter choosed are bad

## Slide 7
Network parameters influence
03
Carole Al Mawla
6 / 16

## Slide 8: Evaluated network scenario
10,000 nodes
BitSimulator + VisualTracer designed for dense networks
Two node placements: homogeneous and heterogeneous
9 flows, creating a congested zone in the middle
1 and 20 packets per flow
Results are reproducible and available on http://eugen.dedu.free.fr/bitsimulator/nanocom24
03
8 / 16

## Slide 9: Investigated parameters
Symbol rate (beta, 𝛽)
  The ratio of time between two consecutive pulses sent and the pulse length Ts / Tp
Communication range
  The effective distance over which communication occurs
Node density
  Number of neighboring nodes per communication range
Pulse duration
03
7 / 16

## Slide 10: Evaluated metrics
Number of packet collisions
Number of packet receptions
Number of packet emissions
Number of packet deliveries to destination
03
8 / 16

## Slide 11: Influence of 𝛽
Increasing 𝛽:
  Reduces the number of packet collisions
  Increases the number of packet receptions and transmissions and deliveries
03
Beta | Collisions | Receptions | Emissions | Deliveries
50 | 513,624 | 342,677 | 5,976 | 103
600 | 62,614 | 812,850 | 6,106 | 270
800 | 62,559 | 812,905 | 6,106 | 270
9 / 16

## Slide 12: Influence of 𝛽
After a certain point (called optimal 𝛽), further maximizing 𝛽 has no effect on the network metrics
03
Beta | Collisions | Receptions | Emissions | Deliveries
50 | 513,624 | 342,677 | 5,976 | 103
600 | 62,614 | 812,850 | 6,106 | 270
800 | 62,559 | 812,905 | 6,106 | 270
1000 | 62,559 | 812,905 | 6,106 | 270
50,000 | 62,559 | 812,905 | 6,106 | 270
10 / 16

## Slide 13: Influence of 𝛽
The optimal value of 𝛽 increases with network density, and depends on the protocol, the number of packets per flow, etc.
03
 | Optimal beta | 
Number of nodes | 1 packet per flow | 20 packet per flow
10,000 | 600 | 600
20,000 | 800 | 800
30,000 | 800 | 800
40,000 | 800 | 1000
11 / 16

## Slide 14: Influence of communication range
Increasing communication range:
  Increases the number of packet collision, transmission, reception, and deliveries
03
Communication range (μm) | Collisions | Receptions | Emissions | Deliveries
285 | 39,960 | 162,733 | 2,807 | 117
350 | 72,730 | 249,519 | 2,969 | 162
450 | 178,075 | 360,315 | 3,016 | 172
12 / 16
Notes: A larger communication range implies more neighboring nodes to fall within reach, consequently, more packets are received, which in turn results in increased retransmissions (emissions) within the relay nodes.

## Slide 15: Influence of node density
Increasing the density:
  Increases the number of packet collisions, transmission, reception, and deliveries
03
Density (nodes) | Collisions | Receptions | Emissions | Deliveries
70 | 8,307 | 195,912 | 2,828 | 157
141 | 62,559 | 812,905 | 6,106 | 270
212 | 315,738 | 1,704,711 | 9,445 | 467
283 | 562,700 | 2,676,558 | 11,280 | 541
13 / 16

## Slide 16: Influence of pulse duration
Increasing the pulse duration:
  Reduces the number of packet collisions
  Increases the number of packet receptions and deliveries
03
Pulse duration (fs) | Collisions | Receptions | Emissions | Deliveries
10 | 72,126 | 150,683 | 2,961 | 89
50 | 57,154 | 164,371 | 2,948 | 94
150 | 32,402 | 189,307 | 2,953 | 100
14 / 16

## Slide 17
Conclusion & Future work
06
Carole Al Mawla
15 / 16

## Slide 18: Conclusion & Future work
Using the perfect algorithm with bad parameters is not ideal
Choosing the optimal parameters enhances network usage
Our future work intends to cover other network parameters and protocols
Carole Al Mawla
06
16 / 16
Parameter | Collisions | Receptions | Emissions | Deliveries
Beta |  |  |  | 
Communication range |  |  |  | 
Density |  |  |  | 
Pulse duration |  |  |  | 

## Slide 19: Thank you!!
Examples with VisualTracer
bs-scenario: bitsimulator --probability 0.02 probaflooding.xml && visualtracer
            bitsimulator --probability 0.01 probaflooding.xml && visualtracer
sim: visualtracer --initialTimeSkip 10000000000, why red nodes behind and not forward?